## Slide 1: Kepler – Best Performance and Best Practices
JWST Transit Planning Meeting
March 11, 2014
Jessie Christiansen
jessie.christiansen@caltech.edu

## Slide 2
How to build an exquisite photometer

## Slide 3
Pointing
    Pre-launch requirement of 3mas (~1 millipixel) pointing jitter in 15 mins
    Measured month to month drift 10-15 millipixels
    Largely eliminated the requirement for absolute flatfielding (large scale flat a geometric model derived from optics)
    Tweaks/sudden impulses are substantially more difficult to cotrend/detrend after the fact (we modified the ADCS to eliminate the drift)
    This will be more of an issue with K2

## Slide 4
Focus
    We’re building an $8b thermometer
    Ideally, separate temperature change timescales from scientific timescales
    As much thermal ancillary data as possible (reaction wheel heaters! etc)
    Tailor photometry method to capture flux – either large apertures or PRF-fitting
    L2/sun shade = excellent
Too
quantized

## Slide 5
Calibration
    Test early, test often
    Don’t scrimp on calibration pixels
- Undershoot was 10x worse when found, but was found early enough in testing that some patches were able to be made
- Moire pattern (resonance in the LDE amplifier circuit), not so much

## Slide 6
Reaction wheels
    Better pointing jitter achieved with higher RPM (Kepler was more stable with three wheels at high RPM than four wheels at low RPM)
    Zero crossings degraded pointing and flux time series – if timing is negotiable, try to keep them away from transits

## Slide 7
Saturation
    Don’t be afraid of saturation!
    (If you have a handle on your non-linearity and you have the ability to capture the spilled charge).
    Theta Cyg (4.5th mag),
    CH Cyg (8th mag)
    Bright TESS and K2 targets should be on the table

## Slide 8
Gotchas
    Provide multiple levels of processing/calibration
    Time system – Kepler AND EPOXI both had trouble
    Accumulation of high-energy particle hits on the detectors (SPSDs, CMEs…)
    Try not to use variable stars as guide stars
    Don’t forget about Jupiter! (And solar system objects in general…)