## Slide 1
pipeline data processing challenges (transits and phase curves)
Dr. Pieter Deroo, Jet Propulsion Laboratory
California Institute of Technology

## Slide 2: Calibration heroics drive exoplanet research
Primary eclipse Size of planet ~ [Rp/Rs]2 ~ 10-2 Transmission Spectrum ~ atm. scaleheight/Rs2 ~ 10-4 -10-3
Secondary eclipse
Emission Spectrum ~ Fp/Fs x [Rp/Rs]2 ~ 10-4-10-3
HST/NICMOS
spectroscopy ~ 1 %
Spitzer/IRS
spectroscopy ~ 1 %
Ground-based
spectroscopy ~ 5 %
Characterizing exoplanet atmospheres is HARD!
Notes: The planet reveals also its molecules, but at a very tiny level, even during the eclipses.
For optimum planets, the size of the planet is at the level of a procent. But to see in the transmission spectrum molecular absorptions, you need an order to two orders of magnitude better precision. You need a precision of 1 part in 10,000. And that number is basically the same for a secondary eclipse, where in NIR, you need about 1:10,000 and in the mid-IR you need 1:1000.
This precision requirement really compares pretty awful to the standard precision advertised for the three avenues explored here.
HST/NICMOS: optimistically 1 % calibrated stability; Spitzer/IRS : realistically, 1% calibrated stablity; Ground-based spectroscopy: a really good night can give you 5% calibrated stability.

## Slide 3
Approach:
optimize the observing mode
identify the systematic errors source
strategy to remove those errors
measure/interpret the spectrum
Emission & Transmission Spectrum ~ 10-4 - 10-3 precision
HST/NICMOS
spectroscopy ~ 1 %
Spitzer/IRS
spectroscopy ~ 1 %
Ground-based
spectroscopy ~ 5 %
Pipeline I
Pipeline II
Notes: How do we get from those awful numbers to the precision required to detect molecules:
The strategy for the three avenues has a lot of similarities.
It basically starts with optimizing the obsersing mode or in other words ‘fully exploring the hardware option’ and all the rest needs to be done in post-processing.
In post-processing, we basically

## Slide 4: No instrument has been designed with combined light requirements in mind (yet!)
Spitzer/IRS secondary eclipse of HD 209458b
Where is the eclipse?
NICMOS secondary eclipse of HD 209458b
Where is the eclipse?
STIS secondary eclipse of HD 189733b
(Evans et al. 2013)
Spitzer photometry secondary eclipse of XO-2
In which panel is the eclipse?
Where is the eclipse?
well-designed, well-performing instruments need significant post-processing if not designed for exoplanet spectroscopy!
(Machalak et al. 2009)

## Slide 5
360° LONGITUDINAL VIEW
Knutson et al. 2007
TRANSMISSION SPECTROSCOPY
Swain et al. 2008
EMISSION SPECTROSCOPY
Grillmair et al. 2008
very exciting science possible, but low numbers
Goal: make this routine
HD 189733b
New science results
Show a deming
INFRARED IMAGE
Majeau et al. 2012
OPTICAL COLOR
Evans et al. 2013

## Slide 6: BUT …
Measurement and revision are hallmark of this field.
With JWST, we want to move beyond that!

## Slide 7: Pipeline and analysis ideas to move forward
Users: Validate and compare ALL elements of the data reduction
Extraction
Instrument characterization
Time series calibration and exoplanet spectrum
focus
T
Blecic et al. 2013
image cleaning algorithms, outlier rejection algorithms, version of the pipeline, background correction used, extraction algorithm, …
Pixel phase map based on which observations, instrument state vector choice, white-light removal, …
Multi-dimensional minimization, stopping criteria, characterization of systematics, …
Kreidberg et al. 2014
IRS handbook

## Slide 8: Pipeline and analysis ideas to move forward
Archive:
Continuously track state-of-the instrument No proprietary time on these instrument characterizing data Need to be able to place each observation in context
  include in meta-data for all observations
  community effort to determine relevant parameters e.g. Knowing scan rate could help spatial scan mode calibration
Improved big-data analysis tools; big-data download tools
  Big data proves useful to characterize instrument, e.g. HST/WFC3 instrument effects; Spitzer phase map construction, etc.
  Current gui’s and query are not optimized for big-data queries:
    All spectral observations of stars of X-th mag
    All meta-data for a month-before and month-after observation
    …
Ability to query the ‘evolution’ of instrument
  Absolute calibration time-line
  Flatfield-timeline
  …

## Slide 9: Pipeline and analysis ideas to move forward
JWST:
Null-test observation very early on for each instrument Multi-object observations might allow this for free If part of other program – make this calibration public soon
  Exoplanet transit ‘null-test’ over 8-hours
  Phase-curve ‘null-test’ over 4-days
ALL:
End-to-end simulation to quantify impact of instrument and calibration on science
  Quantifies impact of instrument, pipeline and analysis tools on retrieved exoplanet characteristics
  Incorporate ‘lessons-learned’ from current instruments ramp effect, detector noise, pixel sensitivity, …
  Calibrate and validate reduction and calibration tools
  Develop a consensus on the best methods to remove unknowns
  Will ready the field pre-launch to optimize JWST return

## Slide 10: Summary:
Exoplanet time-series calibration is hard and has often been controversial
Steps can be taken to improve robustness
  Validation and quantification of ALL steps in the processing
  End-to-End simulations can quantify the impact of processing and instrument on the exoplanet characterization
  Archive tools and scripts can facilitate the development of a ‘holistic’ view of the instrument systematics using big-data tools
  Validate codes and techniques on ‘null-test’ data, either simulated or based on on-orbit observations
We really should not wait until JWST’s launch!